## Slide 1
One-Way Delay over G.703 Contradirectional with xGEnius/Zeus
Guide & Slides corresponding to software ver. 2.10.5
Contradirectional Testing

## Slide 2: Zeus & xGenius
Zeus & xGenius provide deep insights to design, install, maintain, troubleshoot and engineer communications resources of Mobile Operators, Power Utilities, Finance, Labs and R+D centres. The unit is able to verify Ethernet/IP, SyncE, PTP, GbE, IRIG-B, 1PPS, T1/E1, G703, Serial Datacom, C37.94, GOOSE, SV, MMS, Round-trip & One-way Delay tests at all interfaces.
It also has a set of programmable filters to capture live data traffic at wire-speed

## Slide 3: Interfaces & time References
The unit is equipped with GNSS receiver with SMA female connector for connecting an antenna typically supplied with a 5 m of coaxial cable plus a 10 m extension cable.
 | GNSS | PTP | NTP | ToD | IRIG-B | PPS | PP2S | SyncE | T1/E1 | MHz | C.3794
RJ45-A |  | in/out | in/out |  |  |  |  | in/out |  |  | 
RJ45-B |  |  |  |  |  |  |  | in/out |  |  | 
SFP-A |  | in/out | in/out |  |  |  |  | in/out |  |  | 
SFP-B |  |  |  |  |  |  |  | in/out |  |  | 
SFP+A |  | in/out | in/out |  |  |  |  | in/out |  |  | 
SFP+B |  |  |  |  |  |  |  | in/out |  |  | 
BNC-C |  |  |  |  |  |  |  |  | in/out | in/out | 
RJ45-C |  |  |  | in |  | in | in |  | in/out | in/out | 
SMB-C |  |  |  |  |  |  |  |  |  |  | 
SMA | in |  |  |  |  |  |  |  |  |  | 
SMB-1 |  |  |  |  | in | in | in |  |  |  | 
SMB-2 |  |  |  |  | out | out | out |  |  |  | 
RJ-45 |  |  |  | in/out | in/out | in/out | in/out |  | in/out | in/out | 
PHM |  |  |  |  |  |  |  |  |  |  | in/out
PHM
RJ45-C
BNC-C
SFP+ A
SFP+ B
RJ45-A
RJ45-B
SFP-B
SFP-A
Micro SD
SMB-2
SMB-1
SMA
SMB-C
RJ45

## Slide 4: Typical Interconnection
A
G.703 / Codirectional: Endpoints, A and B are identical
B
TX Data + TX Clk
TX Data + TX Clk
C
G.703 / Contradirectional, direct connection: Two kinds of endpoint, C (controlling) and S (subordinated)
S
TX Data
TX Data
S
G.703 / Contradirectional, network connection: Again, identical S (subordinated) endpoints, the network provides the clocks
S
Network
TX Data
RX Data
TX Data
RX Data
TX Clk
RX Clk
TX Clk
RX Clk
TX Clk
RX Clk

## Slide 5: Connecting the GPS & C37.94
Zeus and xGenius are equipped with a G.703/E0 port (PHM22) and a built-in GNSS receiver. Proceed to connect all elements:
Plug the PHM22 module into the slot
Introduce the RJ48 connector to the test port
Connect the cable to the SMA and orient the antenna to open sky.
2
1
2

## Slide 6: Steps to connect the built-in GNSS
Home > Config > Reference clock > Input clock := GNSS (*)
Press LEDS to check the status
Wait for the REF and LOCK LEDs to become green
(*) Go to Home panel, go to Config, the port setup will be displayed then Go to Reference clock and configure Input clock to GNSS.
1
2
1
3

## Slide 7: OCXO or Rubidium
  The unit will be ready for testing LOCK LED is green
  Mind that time is different depending which oscillator xGenius is equipped
Current locking status (Locking, Fine locking, Locked, Holdover, etc.) can be checked in the Reference clock menu.
Metric | OCXO | Rubidium
Locking time | < 5 minutes | < 4 hours
1

## Slide 8: Configuring the GNSS Properties
Configure the GNSS to increase the accuracy:
Config > Reference clock > GNSS receiver > Antenna cable delay to configure a compensation at the correction field
In the same screen Enable/Disable any constellation (GPS, GLONASS, GALILEO, BEIDO) through the Active GNSS setting := GPS…
Go to Fixed‐position mode := Auto-average
1
2
3

## Slide 9: Position Averaging time
GPS has a statistical distribution and averaging for a time filters errors to improve accuracy.
Adjust the Position averaging time and by configuring Auto‐average in the that now displays Averaging
Wait to the Fixed position status to become Active. The unit is now ready for testing.
Note: Theoretically, testing could start before the end of the position averaging process. The improved time estimation due to this function would be automatically applied starting from the end of the auto‐averaging process.
Notes: (a) At least 1h of averaging is required for reasonable accuracy. (b) The procedure should be run only once as long as the location does not change. If any change is detected (longitude, latitude, altitude) an error will be displayed.
1
2

## Slide 10: Holdover mode
When GNSS is not available (i.e. a room without windows) you can first synchronize the unit in a place with GNSS and then go to execute the test in holdover mode.
Accuracy will depend on: (a) the quality of the internal oscillator (Quartz, OCXO, Rubidium); and (b) the holdover period.
Synchronize to GPS and and verify that LED Clock, REF and LOCK are green
Config > Reference clock > Holdover duration := set the time you need for testing
Config > Reference clock > Force holdover := Yes
1
2
3

## Slide 11: Hands-on to Contradirectional test
The testing scenario is a contradirectional network connection. Endpoints are identical (subordinated endpoints). The units measure One-way Delay but other tests are possible:
  Measuring Frequency and Frequency Offset
  Running BER and Performance Tests
  Event Generation and Analysis
  Round trip delay measurement
MUX / Router
GNSS
Generation Analysis
S
S
MUX / Router
GNSS
64 kb/s
contradir
Generation Analysis
64 kb/s
contradir

## Slide 12: Enable the Contradirectional analysis
Configure Home > Config > Mode := G.703/E0 in both endpoints
Configure Home > Config > G.703/E0 := Contradirectional in both endpoints
1
2
2
1

## Slide 13: Configure the Interface
Set Home > Config > G.703/E0 > Clock role := Subordinated in both units
Set Home > Config > G.703/E0 > Line rate := 64 kb/s in both endpoints
In both units, display the LEDs panel and make sure that all LEDs are green
1
2
3

## Slide 14: Enable the OWD test
Configure Test > Delay test > Enable := Yes in both units
Set Test > Delay test > Measurement mode := One way in both testers
1
2
1

## Slide 15: Set the Zero Delay Offset for your Test
Disconnect the units from the network and connect the units back-to-back (*)
In one of the units, set Home > Config > G.703/E0 > Clock role := Controlling
Enable Test > Delay test > Adjust zero offset := Auto calibrate in both units
Configure both units in Subordinated mode again Home > Config > G.703/E0 > Clock role := Subordinated
Reconnect the units to the network
(*) The zero offset setting can be done without having to connect the units together with the help of a physical loopback and setting the unit in “Controlling” mode.
Directly connected
S
C
3

## Slide 16: Running the OWD test
The test is now ready to start then Press RUN
Go to Home > Results > Delay test to check delay results
2
1

## Slide 17: Glossary
AAA: Authentication, Authorization, and Accounting
ACL: Access Control List
AP: Access Point
Busbar: Metallic strip or bar, typically housed inside switchgear, panel boards, and busway enclosures for local high current power distribution C37.94: TDM interface devoted for teleprotection
CB: Circuit Breaker designed to close or open electrical circuit under normal or abnormal conditions. It operates on relays command.
CBWFQ: Class-Based Weighted Fair Queuing
CG: Connected Grid
CID: Individual configuration of each IED CIP: Critical Infrastructure Protection CLI: Command-Line Interface
CorpSS: Corporate Substation
CT: Current Transformer, used for measurement of current, if too high to apply directly to measuring instruments, a CT produces a proportional current which can be measured and recorded, CT are used in metering and protective relays
DAN: Doubly Attached Nodes implementing HSR or PRP
DAU: Data Acquisition Unit
Disconnector: isolates physically and visually the lines
DMZ: Demilitarized Zone
DCB: Directional Comparison Blocking
DCS: distributed control systems
DSC: Differentiated Services Code Point
ESP: Electronic Security Perimeter
Feeder: Transmits power to the distribution points
GM: Grandmaster
GNSS: Global Navigation Satellite System
GOOSE: Generic Object-Oriented Substation Events is a control model defined as per IEC 61850 which provides a fast and reliable mechanism of transferring event data over entire electrical substation networks. When implemented, this model ensures the same event message is received by multiple physical devices using multicast or broadcast services
HMI: Human Machine Interface
PTP: Precision Time Protocol
RedBox: Redundancy Box
Relay: is automatic device which senses an abnormal condition of electrical circuit and closes its contacts and complete the circuit breaker trip.
REP: Resilient Ethernet Protocol
RCT: Redundancy Control Trailer
RTU: Remote Terminal Unit
SA: Substation Automation
SAN: Singly-Attached Node
Secondary Lines: lower voltage side at the substation
SCADA: Supervisory Control And Data Acquisition, transmits and receives data from events of controls, measuring, safety and monitoring. Power system elements can be controlled remotely over. Remote switching, telemetering of grids showing voltage, current, power, direction, consumption in kWh, synchronization.
SCD: Substation Configuration Description SCL: Substation Configuration Language SNTP: Simple Network Time Protocol
Station Bus: Connects the entire substation and helps provide connectivity between central management and individual bays
STP: Spanning Tree Protocol
SV: Sampled Values, is a method to read instantaneous values such as currents, voltages, impedances, etc. from CTs, VTs or digital I/O and then transmitted to make them are available for those IED subscribed.
Switchgear: combination of switches, fuses or CB to control, protect and isolate electrical equipment
SyncE: Synchronous Ethernet
TLV: Type, Length, Value
VT: Voltage Transformer (see CT)Potential Transformer, gives the reference voltage to the Relay for Over-voltage or Under-voltage Protection
UCA IuG: Utility Communications Architecture International Users Group
VDAN: Virtual D
HQoS: Hierarchical Quality of Service
HSR: High-Availability Seamless Redundancy
IA: Industrial Automation
ICS: Industrial control systems
ICU: Intelligent Control Unit
IEC: International Electrotechnical Commission
IEC 61850: Standard defining communication protocols for intelligent electronic devices at electrical substations
IED: Intelligent End Device, microprocessor-based controllers of power system equipment, such as circuit breakers, transformers and capacitor banks to enable advanced power automation.
IRIG: Inter-Range Instrumentation Group
ISE: Identity Services Engine
L3VPN: Layer 3 Virtual Private Network
LA: Lightning Arrester protects the power grid from electric storms
MQC: Modular QoS Command-Line Interface
MMS: Manufacturing Message Specification, messaging system for exchanging real-time data and supervisory control information. Allows client such as SCADA, an OPC server or a gateway to access all IED objects MPLS: Multi-protocol Label Switching
MU: Merging Unit connected to the process bus converts analog data(ie. volts, currect...) into digital information
NERC: North American Electric Reliability Corporation
NIST: National Institute of Standards and Technology
NMS: Network Management System
OAM: Operations and Maintenance
PCP: Priority Code Point
PIOC: Instantaneous overcorrent Protection
PLC: Programmable Logic Controller
PMU: Phasor Measurement Unit
POTT: Permissive Overreaching Transfer Trip
PP: Primary Power
Process Bus: Connects primary units and control equipment to the IEDs
PRP: Parallel Redundancy Protocol
PRTC: Primary Reference Clock
PT: see VT
T-GM: Grand Master PTP
T-BC: Boundary Clock
T-TSC: Slave Clock

## Slide 18
That’s all
www.albedotelecom.com