## Slide 1
RFC 2544 testing with xGenius
Guide & Slides corresponding to software ver. 2.10.5
RFC 2544 test

## Slide 2: Zeus & xGenius
Zeus & xGenius provide deep insights to design, install, maintain, troubleshoot and engineer communications resources of Mobile Operators, Power Utilities, Finace, Labs and R+D centers. The unit is able to verify Ethernet/IP, SyncE, PTP, GbE, IRIG-B, 1PPS, T1/E1, G703, Serial Datacom, C37.94, GOOSE, SV, MMS, Round-trip & One-way Delay tests at all interfaces.
It also has a set of programmable filters to capture live data traffic at wire-speed

## Slide 3: Interfaces & time References
xGenius generates and analyses different kinds of 1544 kb/s and 2048 kb/s signals and also unframed 1544 / 2048 kb/s signals.
PHM
RJ45-C
BNC-C
SFP+ A
SFP+ B
RJ45-A
RJ45-B
SFP-A
Micro SD
SMB-2
SMB-1
SMA
SMB-C
RJ45
SFP-B
 | GNSS | Eth/IP | PTP | NTP | ToD | IRIG-B | PPS | PP2S | SyncE | T1/E1 | MHz | Data
RJ45-A |  | in/out | in/out | in/out |  |  |  |  | in/out |  |  | 
RJ45-B |  | in/out |  |  |  |  |  |  | in/out |  |  | 
SFP-A |  | in/out | in/out | in/out |  |  |  |  | in/out |  |  | 
SFP-B |  | in/out |  |  |  |  |  |  | in/out |  |  | 
SFP+A |  | in/out | in/out | in/out |  |  |  |  | in/out |  |  | 
SFP+B |  | in/out |  |  |  |  |  |  | in/out |  |  | 
BNC-C |  |  |  |  |  |  |  |  |  | in/out | in/out | 
RJ45-C |  |  |  |  | in |  | in | in |  | in/out | in/out | 
SMB-C |  |  |  |  |  |  |  |  |  |  |  | 
SMA | in |  |  |  |  |  |  |  |  |  |  | 
SMB-1 |  |  |  |  |  | in | in | in |  |  |  | 
SMB-2 |  |  |  |  |  | out | out | out |  |  |  | 
RJ-45 |  |  |  |  | in/out | in/out | in/out | in/out |  | in/out | in/out | 
PHM |  |  |  |  |  |  |  |  |  |  |  | in/out

## Slide 4: The RFC 2544
RFC 2544 describes a methodology for testing and evaluating the performance of devices such as routers, switches, and then networks. The RFC 2544 aim is to provide a standardized way to asses the performance in terms of:
Throughput: max. rate can forward traffic without errors
Latency: time for a packet to travel to the destination
Frame Loss: % of pasckets that are lost during the test
Back-to-Back: max. rate at which can receive/transmit frames without errors
These tests are designed to be repeatable and provide a common basis for comparing different devices and Ethernet networks.

## Slide 5: RFC 2544 test
The test described aims to teach how to set up the tester to generate and receive real traffic with specific frames, bit rates, and events. With a few changes it will be possible to evaluate other traffic parameters such as throughput, latency, frame loss rate, etc. The document also describes specific formats for tracing and reporting the results of this test.
Routed Network
1
ALBEDO
xGenius
2
ALBEDO
xGenius
Routed Network
1000BASE-T
1
ALBEDO
xGenius
PHY Loop
Port A
Port B
Port A
Using 2 testers
Test 1
Using 1 tester
Test 2

## Slide 6: Connecting the BNC cables to Port C
xGenius Ports A and B have the connector for the RJ45 cables
xGenius also support optical media and higher bit rates but we are going to execute this test in 1000BASE-T
Connect the Cable to Port A in tester A
Connect the Cable to Port B in tester B
1
1

## Slide 7: Configure the tester
Restore defaults: Home > [System] > Reset to factory settings := Yes
Set operation mode: Home > Test > Mode := Ethernet endpoint
2
1

## Slide 8: Configure the PHY layer Tester 1
Configure the Physical layer in Port A to generate traffic:
Config > Port A > Physical Layer > Connector := Electrical
Config > Port A > Port Mode := Tx/Rx
Results are in Port B in the case we use only one tester:
Config > Port B > Port Mode := Rx
(*) The RFC can also be executed with two testers
3
1

## Slide 9: Configure the RFC
Select RFC 2544, define Objectives:
Test > Performance test := RFC 2544
Config > Port B > Port Mode := LoopBack
(*) If you want just to learn how to program you can use Port A and B of the same tester
3
1

## Slide 10: Configure the RFC 2544
For each separate test:
Test > Performance test > Throughput test := (setup values)
Test > Performance test > Latency test := (setup values)
Test > Performance test > Frame loss test := (setup values)
Test > Performance test > Back-to-back test := (setup values)
Test > Performance test > System recovery test := (setup values)
The unit will inform you about the duration of the RFC test
1
1
2
6
1

## Slide 11: Press RUN
You can spot the frame and the test profile configured at Port B and the type of traffic to be generated at Port A including the flow, the Physical layer, the Ethernet frame, MAC addresses, the PRBS generated, etc.
Press RUN to activate the traffic generation
You can see the activity how the test is progressing Results > Port B > RFC2544
1
2
3

## Slide 12: See Results
You can see the results separately for each test:
Results > Port B > RFC2544 > Throughput
Results > Port B > RFC2544 > Latency
Results > Port B > RFC2544 > Frame loss
Results > Port B > RFC2544 > Back-to-back
Results > Port B > RFC2544 > System recovery
1
1
3
2
1

## Slide 13
That’s all
www.albedotelecom.com