## Slide 1
NTP and TE analysis with xGenius
Guide & Slides corresponding to software ver. 2.3.13
NTP Testing

## Slide 2: xGenius
xGenius provides deep insights to design, install, maintain, troubleshoot and engineer communications resources of Mobile Operators, Power Utilities, Finace, Labs and R+D centers. The unit is able to verify Ethernet/IP, SyncE, NTP, PTP, GbE, IRIG-B, 1PPS, T1/E1, G703, Serial Datacom, C37.94, GOOSE, SV, MMS, Round-trip & One-way Delay tests at all interfaces. It also has a set of programmable filters to capture live data traffic at wire-speed

## Slide 3: Interfaces & time References
The unit is equipped with GNSS receiver with SMA female connector for connecting an antenna typically supplied with a 5 m of coaxial cable plus a 10 m extension cable.
 | GNSS | PTP | NTP | ToD | IRIG-B | PPS | PP2S | SyncE | T1/E1 | MHz | Data
RJ45-A |  | in/out | in/out |  |  |  |  | in/out |  |  | 
RJ45-B |  |  |  |  |  |  |  | in/out |  |  | 
SFP-A |  | in/out | in/out |  |  |  |  | in/out |  |  | 
SFP-B |  |  |  |  |  |  |  | in/out |  |  | 
SFP+A |  | in/out | in/out |  |  |  |  | in/out |  |  | 
SFP+B |  |  |  |  |  |  |  | in/out |  |  | 
BNC-C |  |  |  |  |  |  |  |  | in/out | in/out | 
RJ45-C |  |  |  | in |  | in | in |  | in/out | in/out | 
SMB-C |  |  |  |  |  |  |  |  |  |  | 
SMA | in |  |  |  |  |  |  |  |  |  | 
SMB-1 |  |  |  |  | in | in | in |  |  |  | 
SMB-2 |  |  |  |  | out | out | out |  |  |  | 
RJ-45 |  |  |  | in/out | in/out | in/out | in/out |  | in/out | in/out | 
PHM |  |  |  |  |  |  |  |  |  |  | in/out
PHM
RJ45-C
BNC-C
SFP+ A
SFP+ B
RJ45-A
RJ45-B
SFP-A
Micro SD
SMB-2
SMB-1
SMA
SMB-C
RJ45

## Slide 4: NTP in xGenius & Zeus
This presentation describes how to verify the accuracy and quality of one NTP server.
xGenius and Zeus support NTP server / client emulation using external time references such as GNSS, ToD or IRIG-B (avoid frequency only references such as 1.5/2.0 MHz, 2048 kHz, 1 PPS, SyncE).
NTPv4 maintain 1-20ms time using software-interrupt based solutions over Internet achieving accuracies of 1us or better in ideal conditions.
Network Time Reference
Ethernet
1......p....p....s. / TOD 17:23UTC
ALBEDO
NTP Server
PRTC (Primary Reference Clock)
NTP Client
Ethernet / IP
GNSS
Testing Points
xGenius

## Slide 5: Connecting the antenna & the network
xGenius is equipped with a built-in GNSS receiver. It has a SMA female connector suitable for connecting an antenna. A compact antenna with 5 m of coaxial cable plus a 10 m extension cable. Using a different antenna is possible whenever is compliant with xGenius specifications.
Connect the NTP network to Port A of the xGenius by means of one cable or one optical fiber.
Connect the antenna to the unit oriented to open sky. Some tests may loss accuracy if the number of satellites in sight is limited.

## Slide 6: Steps to connect the built-in GNSS
Home > Config > Reference clock > Input clock := GNSS (*)
Press LEDS to check the status
Wait for the REF and LOCK LEDs to become green
Configure the GNSS parameters
(*) Go to Home panel, go to Config, the port setup will be displayed then Go to Reference clock and configure Input clock to GNSS.
1
2
3
4

## Slide 7: OCXO or Rubidium
  The unit will be ready for testing LOCK LED is green
  Mind that time is different depending which oscillator xGenius is equipped
Note: Current locking status (Locking, Fine locking, Locked, Holdover, etc.) can be checked in the Reference clock menu.
Metric | OCXO | Rubidium
Locking time | < 5 minutes | < 4 hours
1

## Slide 8: Configuring the GNSS Properties
Configure the GNSS to increase the accuracy:
Config > Reference clock > GNSS receiver > Antenna cable delay to configure a compensation at the correction field
In the same screen Enable/Disable any constellation (GPS, GLONASS, GALILEO, BEIDO) through the Active GNSS setting := GPS…
Go to Fixed‐position mode := Auto-average
NOTE: In this mode the equipment uses given spacial GNSS coordinates (longitude, latitude, altitude)
1
2
2
1
3

## Slide 9: Position Averaging time
GPS signal has noise, errors… then averaging is the procedure to improve the accuracy.
Adjust the Position averaging time and by configuring Auto‐average in the that now displays Averaging
Notes: (a) At least 1h of averaging is required for reasonable accuracy, (b) The procedure should be run only once as long as the location does not change. If any change is detected (longitude, latitude, altitude) an error will be displayed.
Wait to the Fixed position status to become Active when the unit will be ready for testing.
Note: Theoretically, testing could start before the end of the position averaging process. The improved time estimation due to this function would be automatically applied starting from the end of the auto‐averaging process.
1
2

## Slide 10: Hands-on to NTP test
xGenius can be configured as a genuine NTP client, no differences at all excepting that xGenius can also qualify the quality of a NTP timing source.
In the pseudo‐slave emulation mode xGenius behaves as a NTP client but keeping an independent synchronization source that enables the unit to calculate parameters such as Time Error (TE) by comparing both timing signals.
NTP server
NTP
Time Reference
NTP Client
Ethernet / IP

## Slide 11: Connecting the tester
In order to connect the xGenius use the RJ‐45 or the SFP to link the network and configure it :
Home > Config > Mode := IP endpoint
Configure the A port > Config > Port A > …
1
2

## Slide 12: Configuring NTP in test Port A
You can configure as NTP Client, Server or Test (also known as pseudo-client):
From the Home > Test > NTP > NTP mode := [None | Server | Client | Test]
Select Test. To verify a Server. A NTP label will appear in top area.
Get the IP address by DHCP: Test > NTP > Dest IPv4 address := Host name
See how IP address is returned
Identify the server to test a name or an IP address
Configure Max/Min polling intervals of the NTP client
1
3
2
5
5
3
4

## Slide 13: Running the Test
Once you have configured the test and the oscillator is locked to the time reference is the moment to execute the test:
Press RUN and test results will began to be computed in real-time
To display NTP results: Home > Results > Port A > NTP
Select the results you want to analyze
i.e. Protocol state
1
2
4
3

## Slide 14: 3 x type of Results (Server & Client mode)
Go to Home > Results > Port A > NTP then, if the tester was configured as Client or Server three different results will be available:
Time Error Statistics
Message statistics: displayed in a table of Rx/Tx message counts
Delay statistics : results depend on the server/client configuration
1
1
2
3

## Slide 15: Time Error results
If you have selected the Test mode (also known as pseudo-client) then Time Error results will be also available otherwise this information will not be available. TE that is computed as the difference between the time provided by NTP server and a reference:
Go to Results > Port A > NTP > Timer error statistics
Check [Current, Average, Min., Max., Std dev] results
.
2

## Slide 16: Event logger enable
Global counts, statistics and LEDs provide information about which events and how many of them have been registered but they do not say too much about how they are distributed in time. These information is supplied at the Event Logger a graphical representation tool that permits to trace the evolution of key parameters.
The first thing to to is to enable it:
Go to Home > Test > Event logger setup
Set Enable := Yes
1
1

## Slide 17: Configuring the Event Logger
Traceable Events are categorized in different classes. Moreover, each test port has its own traceable events. These events may be different for each test port.
Clear the currently selected filters: Clear all filters := Yes
Select the Port A or Port B
Choose the events to trace: Anomalies/defects | Bandwidth statistics | Frame layer statistics | SLA statistics | BERT | PTP | NTP | Synchronization
Press Run to begin the generation of a trace file
1
3
2
4

## Slide 18: Display the logs
With the Event Logger you can select one or various events and trace them so that all changes along with the time and date these changes are registered are recorded with a 1 second resolution. The event logger provides representations and zoom levels to enable event analysis at different time scales:
Go to Results > Event logger
To select a saved trace double click at (…) to display the folder of traces
Select and Open one of the files
1
2
3
3

## Slide 19: Event logger results
You can display the trace of the evolution of the previously selected parameters:
View and analyze the details of the histogram
Set the scale at your preferred zoom level
Selected one event to display a more detailed diagram
Click on the screen to know the exact value at one specific time
4
4
6
2
2
2
1
3

## Slide 20: Scaling the trace
To change the scale horizontally click one time, for vertical two times
Click in the red buttom and draw to the left or to the right
To change the scale vertically click two times
To move the trace across the time click one of the three the red buttoms and draw the finger up and down
Click in the auto-scale symbol to return to the initial conditions
1
1
2
1
5

## Slide 21: Exporting Logs
To export log files in CSV format:
Go Home > [File icon] > Configuration files | Report files > Internal memory to list the files currently stored in the unit
Select the files you want to export: File name > Export
Choose an external device: micro SD | USB
If no external device a popup will appear: ‘No devices present’
2
3
1
1

## Slide 22: Glossary
AAA: Authentication, Authorization, and Accounting
ACL: Access Control List
AP: Access Point
Busbar: Metallic strip or bar, typically housed inside switchgear, panel boards, and busway enclosures for local high current power distribution C37.94: TDM interface devoted for teleprotection
CB: Circuit Breaker designed to close or open electrical circuit under normal or abnormal conditions. It operates on relays command.
CBWFQ: Class-Based Weighted Fair Queuing
CG: Connected Grid
CID: Individual configuration of each IED CIP: Critical Infrastructure Protection CLI: Command-Line Interface
CorpSS: Corporate Substation
CT: Current Transformer, used for measurement of current, if too high to apply directly to measuring instruments, a CT produces a proportional current which can be measured and recorded, CT are used in metering and protective relays
DAN: Doubly Attached Nodes implementing HSR or PRP
DAU: Data Acquisition Unit
Disconnector: isolates physically and visually the lines
DMZ: Demilitarized Zone
DCB: Directional Comparison Blocking
DCS: distributed control systems
DSC: Differentiated Services Code Point
ESP: Electronic Security Perimeter
Feeder: Transmits power to the distribution points
GM: Grandmaster
GNSS: Global Navigation Satellite System
GOOSE: Generic Object-Oriented Substation Events is a control model defined as per IEC 61850 which provides a fast and reliable mechanism of transferring event data over entire electrical substation networks. When implemented, this model ensures the same event message is received by multiple physical devices using multicast or broadcast services
HMI: Human Machine Interface
PTP: Precision Time Protocol
RedBox: Redundancy Box
Relay: is automatic device which senses an abnormal condition of electrical circuit and closes its contacts and complete the circuit breaker trip.
REP: Resilient Ethernet Protocol
RCT: Redundancy Control Trailer
RTU: Remote Terminal Unit
SA: Substation Automation
SAN: Singly-Attached Node
Secondary Lines: lower voltage side at the substation
SCADA: Supervisory Control And Data Acquisition, transmits and receives data from events of controls, measuring, safety and monitoring. Power system elements can be controlled remotely over. Remote switching, telemetering of grids showing voltage, current, power, direction, consumption in kWh, synchronization.
SCD: Substation Configuration Description SCL: Substation Configuration Language SNTP: Simple Network Time Protocol
Station Bus: Connects the entire substation and helps provide connectivity between central management and individual bays
STP: Spanning Tree Protocol
SV: Sampled Values, is a method to read instantaneous values such as currents, voltages, impedances, etc. from CTs, VTs or digital I/O and then transmitted to make them are available for those IED subscribed.
Switchgear: combination of switches, fuses or CB to control, protect and isolate electrical equipment
SyncE: Synchronous Ethernet
TLV: Type, Length, Value
VT: Voltage Transformer (see CT)Potential Transformer, gives the reference voltage to the Relay for Over-voltage or Under-voltage Protection
UCA IuG: Utility Communications Architecture International Users Group
VDAN: Virtual D
HQoS: Hierarchical Quality of Service
HSR: High-Availability Seamless Redundancy
IA: Industrial Automation
ICS: Industrial control systems
ICU: Intelligent Control Unit
IEC: International Electrotechnical Commission
IEC 61850: Standard defining communication protocols for intelligent electronic devices at electrical substations
IED: Intelligent End Device, microprocessor-based controllers of power system equipment, such as circuit breakers, transformers and capacitor banks to enable advanced power automation.
IRIG: Inter-Range Instrumentation Group
ISE: Identity Services Engine
L3VPN: Layer 3 Virtual Private Network
LA: Lightning Arrester protects the power grid from electric storms
MQC: Modular QoS Command-Line Interface
MMS: Manufacturing Message Specification, messaging system for exchanging real-time data and supervisory control information. Allows client such as SCADA, an OPC server or a gateway to access all IED objects MPLS: Multi-protocol Label Switching
MU: Merging Unit connected to the process bus converts analog data(ie. volts, currect...) into digital information
NERC: North American Electric Reliability Corporation
NIST: National Institute of Standards and Technology
NMS: Network Management System
OAM: Operations and Maintenance
PCP: Priority Code Point
PIOC: Instantaneous overcorrent Protection
PLC: Programmable Logic Controller
PMU: Phasor Measurement Unit
POTT: Permissive Overreaching Transfer Trip
PP: Primary Power
Process Bus: Connects primary units and control equipment to the IEDs
PRP: Parallel Redundancy Protocol
PRTC: Primary Reference Clock
PT: see VT
T-GM: Grand Master PTP
T-BC: Boundary Clock
T-TSC: Slave Clock

## Slide 23
That’s all
www.albedotelecom.com